## Slide 1
The role of vertically-pointing Ka-band radar in studies
of precipitation processes using SAIL/SPLASH data
Sergey Y. Matrosov
CIRES, University of Colorado and NOAA Physical Sciences Laboratory

## Slide 2
SAIL Ka-band ARM zenith-pointing radar (KAZR)
is a useful tool for retrieving solid (and liquid) precipitation properties
KAZR data can be used for high temporal and
vertical resolution estimates of snowfall rate,
ice water content, characteristic size of falling snowflakes, their degrees of riming
Synergy of KAZR measurements with radar
data at other frequencies available at SAIL/SPLASH allows for more robust retrievals of snowfall
microphysical parameters (e.g., snowflake size)
Examples of KAZR reflectivity measurements in SAIL/SPLASH

## Slide 3
SAIL KAZR was previously used in MOSAiC to derive high
temporal (~ 30 sec) resolution snowfall rate estimates

## Slide 4
Radar-based retrievals of mean precipitation (snowfall) rate (S)
and cloud ice water path (IWP) combined with concurrent MWR-based estimates of integrated water vapor (IWV) and supercooled liquid water content (LWP) can be used for evaluating moisture conversion processes in the atmosphere

## Slide 5
Potential SAIL/SPLASH KAZR – scanning X-band radar synergy
(a Ka-S band example)
height
Time, hours
0
24
Oue et al. 2023
height
Ka-band (SUNY)
S-band (WSR-88D KOKX)
Modeling S-Ka-band DWR vs
snowflake characteristic size
2018/01/04

## Slide 6
Potential SAIL/SPLASH W-X-band scanning radar synergy

## Slide 7
An example of using a STSR polarimetric
precipitation radar for estimating particle shapes
(an approach applicable to X-band radars)
KDLH radar scan at 4.5deg on 5 March 2013 at 19:27 UTC

## Slide 8
ARM zenith-pointing radar measurements provide information for high spatial
and temporal resolution retrievals of snowfall microphysics and QPE
Multi-sensor retrievals (e.g., KAZR + MWR) allow for simultaneous estimates
of precipitation, cloud and water vapor parameters providing a framework for
better understanding the efficiency of atmospheric moisture conversion
Combination of measurements at different radar frequencies available at SAIL-SPLASH
can be used to improve retrievals of cloud and precipitation microphysical parameters
Conclusions