## Slide 1: How much snow sublimated during the Winter of 2022-2023?
Measuring and modeling seasonal sublimation with measurements from the SoS campaign
…and ideas for collaborating with the SAIL and SPLASH Campaigns
elilouis@uw.edu
Notes: Motivation:
- The mystery of missing water in the Colorado river – per unit of precip, less water is ending up as streamflow
- Some have hypothesized that sublimation could be the cause of this missing water – some model runs in the UCRB have estimated 40% of the snowpack is lost to sublimation

## Slide 2: Research Questions
How much sublimation did we measure at Kettle Ponds over the 2022-23 snow season? How much sublimation occurs during blowing snow and non-blowing snow conditions?
How do estimates by the eddy covariance measurements and mean-profile (MOST/bulk aerodynamic) methods compare?
elilouis@uw.edu

## Slide 3: Measuring seasonal cumulative sublimation
~3 – 5% of winter precipitation (702mm) (5-8% of seasonal max SWE, 437mm)
EC
Seasonal cumulative sublimation (mm SWE)
elilouis@uw.edu
Notes: EXTRA NOTES:
  We measured sublimation during the “snow-on” season, which we define as the time period with complete snow cover at Kettle Ponds, approximately November 30 to May 10
  Precipitation was measured by SPLASH/NOAH (Tilden’s dataset, precip guage with the Wyoming shield)
  SWE measured with SOS’ C tower snow pillow
  Sublimation during blowing snow includes 5-minute measurements where either of the two FlowCapt sensor measured any blowing snow flow. The FlowCapt sensor appears to be sensitive even at its detection threshold of 0.01 g/m^2/s (instrument is accurate to 0.01).

## Slide 4: Measuring seasonal cumulative sublimation
accounted for ~43% of moisture lost
~3 – 5% of winter precipitation (702mm) (5-8% of seasonal max SWE, 437mm)
Sublimation during blowing snow
FlowCapt blowing snow sensor
EC
Blowing Snow
Daily sublimation
(mm SWE)
Seasonal cumulative sublimation (mm SWE)
elilouis@uw.edu
Notes: EXTRA NOTES:
  We measured sublimation during the “snow-on” season, which we define as the time period with complete snow cover at Kettle Ponds, approximately November 30 to May 10
  Precipitation was measured by SPLASH/NOAH (Tilden’s dataset, precip guage with the Wyoming shield)
  SWE measured with SOS’ C tower snow pillow
  Sublimation during blowing snow includes 5-minute measurements where either of the two FlowCapt sensor measured any blowing snow flow. The FlowCapt sensor appears to be sensitive even at its detection threshold of 0.01 g/m^2/s (instrument is accurate to 0.01).

## Slide 5: Measuring seasonal cumulative sublimation
accounted for ~43% of moisture lost
~3 – 5% of winter precipitation (702mm) (5-8% of seasonal max SWE, 437mm)
Sublimation during blowing snow
FlowCapt blowing snow sensor
EC
Blowing Snow
Daily sublimation
(mm SWE)
Seasonal cumulative sublimation (mm SWE)
Sublimation cannot account for missing CO river water?
elilouis@uw.edu
Notes: EXTRA NOTES:
  We measured sublimation during the “snow-on” season, which we define as the time period with complete snow cover at Kettle Ponds, approximately November 30 to May 10
  Precipitation was measured by SPLASH/NOAH (Tilden’s dataset, precip guage with the Wyoming shield)
  SWE measured with SOS’ C tower snow pillow
  Sublimation during blowing snow includes 5-minute measurements where either of the two FlowCapt sensor measured any blowing snow flow. The FlowCapt sensor appears to be sensitive even at its detection threshold of 0.01 g/m^2/s (instrument is accurate to 0.01).

## Slide 6
MOST Ensemble
SOS EC measurements
Modeling seasonal cumulative sublimation
Min model run 33.7mm
max model run 149mm
Use “offline” turbulence method (Monin Obukhov Similarity Theory) to run model ensemble (n=240) (Lapo, 2018)
  Many different stability functions
  Range of z0, 1e-5 to 1e-3
  Multiple surface temperature measurements
Models estimate between 5 – 21% of winter precipitation (702mm)
elilouis@uw.edu
Notes: Extra Notes:
…or… 8-34% of seasonal max SWE (437mm)
Lowest model - Louis b = 12 Tsurf_c e_sat_alduchov 1e-05 – 33.7
Highest model - MO Beljaars Holtslag Tsurf_rad_d e_sat_metpy 0.001 148.754604

## Slide 7
MOST Ensemble
SOS EC measurements
Modeling seasonal cumulative sublimation
Min model run 33.7mm
max model run 149mm
Z0=1e-3
Z0=1e-4
Z0=1e-5
Use “offline” turbulence method (Monin Obukhov Similarity Theory) to run model ensemble (n=240) (Lapo, 2018)
  Many different stability functions
  Range of z0, 1e-5 to 1e-3
  Multiple surface temperature measurements
Models estimate between 5 – 21% of winter precipitation (702mm)
Models very sensitive to z0, insensitive to stability function
Models sensitive to Ts
elilouis@uw.edu

## Slide 8
Focus on 2 model runs that (relatively) closely match measurements, varying only by surface temperature measurement used (Pyrgeometer vs LW Radiometer)
Modeling seasonal cumulative sublimation
Pyrgeometer
LW radiometer
Seasonal cumulative sublimation estimated by 2 model runs,
varying only by the input Ts measurement
SOS Measured

## Slide 9
Modeling seasonal cumulative sublimation
Pyrgeometer
LW radiometer
Seasonal cumulative sublimation estimated by 2 model runs,
varying only by the input Ts measurement
SOS Measured
Why do surface temperatures matter?
Focus on 2 model runs that (relatively) closely match measurements, varying only by surface temperature measurement used (Pyrgeometer vs LW Radiometer)

## Slide 10
Modeling seasonal cumulative sublimation
Saturation vapor pressure curve
Pyrgeometer
LW radiometer
Seasonal cumulative sublimation estimated by 2 model runs,
varying only by the input Ts measurement
SOS Measured
Focus on 2 model runs that (relatively) closely match measurements, varying only by surface temperature measurement used (Pyrgeometer vs LW Radiometer)
MOST states that sublimation ∝ vapor pressure gradient, which depends on the saturated vapor pressure at the snow surface, a function of Ts
Notes: In the case of these two model runs, the different T_s measurements result in a 150% increase in estimated sublimation (although that only means an increase from 5.7 to 8.5% of total winter precip)
What we're seeing here is the effect of the surface temperature sensors measuring different temperatures...

## Slide 11
Modeling seasonal cumulative sublimation
We observed frequent disagreement between temperatures calculated using the pyrgeometer and the downward-facing LW radiometer
And small differences in surface temperature result in significant differences in near-surface vapor pressure gradient
Surface temp. (Ts)
measurements,
Feb. 1-2, 2023
Pyrgeometer
LW radiometer
Nighttime vapor pressure profile based on two measures of Ts
elilouis@uw.edu
Notes: So why do we care? We see that turbulent fluxes calculated with MOST are sensitive to surface temperatures. If our two measurements of surface temperature disagree enough to change the total seasonal sublimation, than we can be pretty sure that models (like VIC, NoahMP), which often get surface temperature very wrong, are in part unable to correctly predict sublimation because of incorrect surface temperature.
EXTRA NOTES:
The profiles shown are from 2000 (8pm) on February 2nd

## Slide 12
Modeling seasonal cumulative sublimation
Modeled and measured latent heat flux,
January 19, 2023
Model run using
Pyrgeometer
Model run using
LW radiometer
This is what the difference in choice of Ts measurement looks like on a single day
Switching gears slightly…
SOS Measured
Notes: All of this uncertainty leads us to two thoughts –
one, it would be nice to have more measurements of sublimation,
and two, it would be nice to have more measurements of surface temperature…

## Slide 13
Modeling seasonal cumulative sublimation
Modeled and measured latent heat flux,
January 19, 2023
Measured latent heat flux as multiple sites,
January 19, 2023
Model run using
Pyrgeometer
Model run using
LW radiometer
SOS Measured
Differences in turbulence measurements across sites/campaigns are of similar order of magnitude as differences in modeled sublimation due to different Ts measurements
Different amounts of noise in measurements indicate that cleaning/preprocessing methods influence calculated turbulent fluxes
This is what the difference in choice of Ts measurement looks like on a single day
Switching gears slightly…

## Slide 14: Measuring seasonal cumulative sublimation… again
MOST Ensemble
SOS, Kettle Ponds
SAIL ECOR, Gothic
SAIL ECOR, Kettle Ponds
SAIL turbulent flux measurements result in very close sublimation estimates despite being ~2km away
More variability in turb. flux measurements that are all at the same site
elilouis@uw.edu

## Slide 15
Incorporating SAIL and SPLASH measurements
Moving forward:
  Calculate z0 for the study sites, identify the “best” MOST model runs
  Explore hypothesis that EC measurements under-measure surface fluxes –
    Why does MOST almost always overestimates sublimation?
    Could lateral advection of moisture mean that EC measurements to not represent the surface flux?
Ideas for collaboration:
  Compile all raw turbulent flux measurements, apply same processing/cleaning steps
  Use MEP model to calculate sublimation
  Compile all Ts measurements, explore novel methods for estimating Ts
  Examine land surface model runs, compare estimated and measured Ts
elilouis@uw.edu
Stossel box/
lysimeter
Eddy
Covariance
12pm
12pm
Winter (Feb 2)
Spring (Mar 30)
Daily sublimation measured two ways
Vertical profiles of Latent heat flux, Kettle Ponds
Stossel box

## Slide 16: References
Abatzoglou, J. T., Rallings, A., Bernacchi, L., Viers, J. & Medellín-Azuara, J. California’s Missing Forecast Flows in Spring 2021 – Challenges for seasonal flow forecasting. California WaterBlog https://californiawaterblog.com/2021/07/18/californias-missing-forecast-flows-in-spring-2021-challenges-for-seasonal-flow-forecasting/ (2021).
Alduchov, O. A. & Eskridge, R. E. Improved Magnus form approximation of saturation vapor pressure. J. Appl. Meteorol. 35, 601–609 (1996).
Bolton, D., 1980: The computation of equivalent potential temperature. Mon. Wea. Rev., 108.
Lapo, K. E. (2018). Turbpy Python package for simulating turbulence. Seattle, WA: University of Washington. https://doi.org/10.5281/ zenodo.1421061
elilouis@uw.edu

## Slide 17: Seasonal cumulative sublimation estimates using different surface temperature measurements (RQ3)
Measured
Only looking at lowest model runs (z0=1e-5)
Choice of temperature sensor influences modeled sublimation due to systematic cold-bias at night of the Pyrgeometer, and its occasional cold bias during daytime
Choice of esat curve matters (for calculating saturated vapor pressure at snow surface from surface temperature)
Pyregometer
LW Radiometer
Alduchov (1996)
Bolton (1980)

## Slide 18: Seasonal cumulative sublimation estimates using different surface temperature measurements (RQ3)
Measured (EC)
Look at model runs with z0=1e-5, selecting one stability function for simplicity (limiting to n=4 model runs)
Choice of temperature sensor influences modeled sublimation due to systematic cold-bias at night of the Pyrgeometer, and its occasional cold bias during daytime
Choice of esat curve matters (for calculating saturated vapor pressure at snow surface from surface temperature) – especially during winter-time, when near-surface vapor pressure gradients are small
Pyregometer
LW Radiometer
Alduchov (1996)
Bolton (1980)
February 1, 2023
March 28, 2023
Alduchov (1996)
Bolton (1980)

## Slide 19: Effect of sat vapor pressure curve
esat Bolton (1980)
esat Alduchov (1996)
Ts measurement
Pyrgeometer