## Slide 1: UAS-Based Observations of Surface Properties During SPLASH
Gijs de Boer
Janet Intrieri
Jonathan Hamilton
Darren Jackson
Jack Elston
Maciej Stachura
Jake Longenecker
Michael Rhodes
Brian Argrow

## Slide 2: Traditional Surface Sensing

## Slide 3: Traditional Surface Sensing

## Slide 4: UAS/Sensor Systems and Deployment Timeline
Stabilized Kipp and Zonen Pyranometer (x2)
RedEdge-MX 5 channel Camera
University of Colorado HELiX (left) deployed with custom Kipp and Zonen PR-1 Pyranometers and multispectral camera to measure up- and downwelling shortwave irradiance, albedo, surface features, NDVI, and more.
Deployments in March, April, May, and June 2022.
Observed impacts of dust on snow and surface albedo evolution over spatial area.

## Slide 5: Evolution of Surface Albedo
03/13
03/14
03/15
03/16
04/19
04/20
04/21
04/22
03/17
05/11
05/12
05/13
05/14
Date (mm/dd) 2022
Albedo
0
1
0.2
0.4
0.6
0.8
Mean
10 25 75 100
HELiX
Avery ASFS
KP ASFS

## Slide 6: Influence of Dust on Snow
04/18
04/19
04/20
04/21
03/12-03/16
Significant snow melt was observed during the April deployment. During this time, dust that had previously been deposited in the snowpack emerged at the surface, and the snowpack became significantly wetter. Together, these events resulted in a substantial reduction of the snow surface albedo. March flights showed albedos in this area of around 0.8, while the April albedos decreased from around 0.65 to 0.45 over the course of four days. Additionally, the river began to open up, resulting in even lower albedos values (<0.4). All flights in these figures were conducted around 10 am MDT.
Albedo
Albedo

## Slide 7: Scale-Dependent Representative Albedo Values

## Slide 8: Scale-Dependent Representative Albedo Values
03/20
03/30
04/09
04/19
04/29
05/09
05/19
05/29

## Slide 9: Scale-Dependent Representative Albedo Values

## Slide 10: Albedo of Different Features

## Slide 11: Albedo of Treed Areas
Early In Flight / Late In Flight 
Downwelling SW Irradiance (W/m2)
Initial evaluation of HRRR simulations appears to show that the HRRR surface albedo is significantly lower than observed. As a result, a question was posed about the influence of the mix of surface cover on grid-box-scale albedo. Using the HELiX, we flew over different surface types to understand the individual contributions of different types of surfaces and vegetations while the underlying is snow-covered.

## Slide 12: UAS/Sensor Systems and Deployment Timeline
Black Swift Technologies S2 (left) and E2 (above) deployed with L-band radiometer and multispectral camera to measure soil volumetric water content, surface temperature, surface elevation and NDVI.
Deployments in mid-October, early June, and early September for two years.

## Slide 13: Advancing Technical Readiness
With funding from the NOAA Weather Program Office, our team has worked to deploy and evaluate the performance of Black Swift Technologies UAS-based soil moisture sensing capabilities. The system includes an L-band radiometer to detect soil moisture levels in the top ~5 cm of the surface.
As part of this work, the payload was deployed on a new UAS platform (E2). Additionally, sensor thermal stability was improved, resulting in more consistent soil moisture measurements. This has helped advance an off-the-shelf sensor system.

## Slide 14: Mapping Soil Moisture and Other Surface Properties

## Slide 15: Mapping Soil Moisture and Other Surface Properties

## Slide 16: Summary
UAS were deployed in SPLASH to collect information on the spatial and temporal evolution of surface properties, including albedo, soil moisture, elevation, temperature, and NDVI.
Datasets are published and available to the public through Zenodo.
Significant technological advancements were made as a part of this work, improving system readiness and commercial viability.
Conducting flights throughout the year would help provide a detailed perspective on the complexities associated with the seasonal evolution of key properties.